## Slide 1: Hitcon Badge BLE explain V1.4
Adding AES

## Slide 2
Wallet Address
Initialize + Re-paring
BLE AES Key
QR-Code
格式:
Hitcon://pair?v=版本數
&a=錢包Address
&k=AES Key
&s=ServiceUUID
&c=Characteristic前四個Byte[6]
初始化的時候，
Badge會將生成好的Public Address和BLE Key打包成一個網址顯示在QR Code上面
BLE 各charastic UUID前4byte
Example:
hitcon://pair?
v=18&
a=808c2257d778e5f1340d9325116f5a7273b33f5d&
k=09626aa096254e8a8ce871bfd7b8895c&
s=1cbfbb33-ffc7-c966-77f9-311c6ba9e425&
c=26ccce12e2c66a0b72c50cca509dbfc1275074f57e7c5668
BLE Service UUID

## Slide 3
QR-Code
generate
Initialize + Re-paring Flow
User Request for Reparing or
First time config
Reset
Wait for connection
Main Menu
MT7697沒辦法 on-line修改BLE，
所以必須Reset一次

## Slide 4
UUIDs
為了避免濫發交易訊息，UUID是綁定時隨機產生的
QR Code會寫Characteristic UUID的前4個Byte，後面的UUID與Service相同
QRcode的Characteristic順序如下:
Transaction
Txn
AddERC20
Balance
General Purpose Cmd
General Purpose Data

## Slide 5
AES enc
Raw Data
AES encryption
16Byte Random IV
Enc Data
Enc Data
16Byte Random IV
Payload
Write to GATT
Append to 128 Byte

## Slide 6
BLE Spec
MTU Size: 144+3 byte
No Device Name
Broadcast: 128bit Service UUID only

## Slide 7
Adding ERC20 Support
1.Contract Address
2.TotalSupply Method
3.BalanceOf Method
4.Transfer Method
5.TransferFrom Method
6.Approve Method
7.Token縮寫
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x10 0x14 0xADDRESS20BYTE
0x11 0x04 [Method]
…
…
0x17
AES encryption
Write to AddERC20 Gatt

## Slide 8
Transaction
1.To Address
2.Value
3.Gas Price
4.Gas limit
5.Noice
6.Data
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 0xADDRESS20BYTE
0x02 Value_len Value
…
…
0x06
AES encryption
Write to Transaction Gatt
Badge notify
Txn Gatt
Txn Broadcast
Big endian for all data

## Slide 9
ERC20 Transaction
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 0xADDRESS20BYTE
0x02 Value_len Value
…
…
0x06
AES encryption
Txn Broadcast
自己把ERC20的Data帶進去，Badge會Parsing這部分的Data顯示出來
1.To Address
2.Value
3.Gas Price
4.Gas limit
5.Noice
6.Data
Write to Transaction Gatt
Badge notify
Txn Gatt
Big endian for all data

## Slide 10
Update Balance
Value
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 Wallet_Address
0x02 0x08 Value
AES encryption
Write to Balance_Gatt
1.Wallet_Address
2.Value
Type(value) = Double

## Slide 11
Update ERC20 Balance
Value
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 Contract Address
0x02 0x08 Value
AES encryption
1.Contract Addr
2.Value
Write to Balance_Gatt
Type(value) = Double