## Slide 1: Hitcon Badge BLE explain V1.1

## Slide 2
Wallet Address
Initialize
BLE AES Key
QR-Code
格式:
Hitcon://?v=版本數
&a=錢包Address
&k=AES Key
&s=ServiceUUID前四個Byte
&c=Characteristic前四個Byte[6]
初始化的時候，
Badge會將生成好的Public Address和BLE Key打包成一個網址顯示在QR Code上面
BLE Service UUID前4byte
BLE 各charastic UUID前4byte
Example:
Hitcon://?v=18
&a=808c2257d778e5f1340d9325116f5a7273b33f5d
&k=41e77dcd1d10df31d2f143b88e563693
&s=c49aec31
&c=a3ae3cde7b5e9feff77a6f0dffb017590a5527c9e8a1dc52

## Slide 3
Wallet Address
Re-paring
BLE AES Key
QR-Code
格式:
Hitcon://?v=版本數
&a=錢包Address
&k=AES Key
&s=ServiceUUID前四個Byte
&c=Characteristic前四個Byte[6]
重新綁定的時候，
Badge會將生成好的Public Address和BLE Key打包成一個網址顯示在QR Code上面
BLE Service UUID前4byte
BLE 各charastic UUID前4byte
Example:
Hitcon://?v=18
&a=808c2257d778e5f1340d9325116f5a7273b33f5d
&k=41e77dcd1d10df31d2f143b88e563693
&s=c49aec31
&c=a3ae3cde7b5e9feff77a6f0dffb017590a5527c9e8a1dc52

## Slide 4
UUIDs
為了避免濫發交易訊息，UUID是綁定時隨機產生的
QR Code會寫UUID的前4個Byte
QRcode的Characteristic順序如下:
Transaction
Txn
AddERC20
Balance
General Purpose Cmd
General Purpose Data

## Slide 5
Adding ERC20 Support
1.Contract Address
2.TotalSupply Method
3.BalanceOf Method
4.Transfer Method
5.TransferFrom Method
6.Approve Method
7.Token縮寫
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x10 0x14 0xADDRESS20BYTE
0x11 0x04 [Method]
…
…
0x17
AES encryption
Write to AddERC20 Gatt

## Slide 6
Transaction
1.To Address
2.Value
3.Gas Price
4.Gas limit
5.Noice
6.Data
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 0xADDRESS20BYTE
0x02 Value_len Value
…
…
0x06
AES encryption
Write to Transaction Gatt
Badge notify by
Txn Gatt
Txn Broadcast
Big endian for all data

## Slide 7
ERC20 Transaction
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 0xADDRESS20BYTE
0x02 Value_len Value
…
…
0x06
AES encryption
Txn Broadcast
自己把ERC20的Data帶進去，Badge會Parsing這部分的Data顯示出來
1.To Address
2.Value
3.Gas Price
4.Gas limit
5.Noice
6.Data
Write to Transaction Gatt
Badge notify by
Txn Gatt
Big endian for all data

## Slide 8
Update Balance
Value
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 Wallet_Address
0x02 Value_len Value
AES encryption
Write to Balance_Gatt
1.Wallet_Address
2.Value

## Slide 9
Update ERC20 Balance
Value
Encode
Format:
Header(uint8_t) length(uint8_t) Data[len]
0x01 0x14 Contract Address
0x02 Value_len Value
AES encryption
1.Contract Addr
2.Value
Write to Balance_Gatt